## Slide 1
Democritus
University
Of
Thrace

## Slide 2
Team : SystemsGenesys
Mentor: Dr. Rantos Konstantinos
Member: Batzolis Eleftherios
Projects: 1) Stealthy Logic: Keyboard Injection to Verilog State Machine Trojan for Conditional DoS
2) Cryptoleak: Subtle Timing Exploits for AES Key Extraction with Trojan Listeners

## Slide 3
Method for adding the vulnerability
We will use OpenAI’s ChatGPT because:
It’s highly sophisticated
Is versatile and has depth of Knowledge
Has natural, Context-Aware Conversations
Offers integration with other Tools via API
Has good coding capabilities
Is considered as a cutting-edge LLM
ChatGPT o1

## Slide 4
Prompt Engineering
I will use the Chain Of Thought(CoT) technique because:
Digital design is a really complex task that requires complex reasoning an produces context aware responses.
These tasks (like creating an FSM) require multiple intermediate reasoning steps.

## Slide 5
Prompting Pattern
In order to gather the necessary steps to create a hardware trojan using an LLM, we enhanced our prompt engineering techniques first by using the Recipe prompt pattern
Prompt example: https://chat.openai.com/share/44e37758-e3c0-4025-98a8-89f75f36166b

## Slide 6
Prompting Pattern
https://chatgpt.com/share/670fff2a-2b88-800b-aec3-a39d06cac69f
Visualization-of-Thought
•Enhances Problem-Solving
•Improves Communication
•Increases Transparency
•Facilitates Better Decision-Making
•Boosts Code capabilities

## Slide 7
Prompting Pattern
We then used the Persona prompt pattern :
In order to provide the LLM with intent
Provide the LLM with motivation to achieve a certain task.
Structure fundamental contextual statements around key ideas
Provide example code for the LLM to follow along by using the Chain of Thought prompt engineering technique.
Prompt example: https://chat.openai.com/share/8d425e27-d6d8-473b-9f53-7e42fdf6c008

## Slide 8
During our research, the efforts of writing “malicious” code was inhibited by the content filtering process ChatGPT has. We discovered two ways to bypass and “exploit” the Reinforcement learning from human feedback (RLHF) and openAI’s content filtering by using YACATEC MAYA as a primary language . We share a conversation bellow as a Proof of Concept.
Asking how to build a chemical bomb using English:
https://chat.openai.com/share/445456a6-b89d-438b-a547-05adbec612de
Asking how to build a chemical bomb using Yucatec Maya:
https://chatgpt.com/share/670ff0da-9960-800b-bb94-a1ea10787bb7
We discovered an exploit of ChatGPT RLHF/content filtering process

## Slide 9
We discovered a second exploit of ChatGPT RLHF/content filtering process
By using prompt engineering, and specifically the “persona” pattern we managed to bypass the RLHF/content filtering process.
Prompt cannot be shared due to moderation unfortunately:

## Slide 10
We created a working keystroke injection tool, commonly referred to as a BadUSB.
Similar in functionality to the well-known USB Rubber Ducky by Hak5, it offers extensive capabilities at a lower cost and is fully open-source.
Despite resembling a standard USB flash drive, it functions as a keyboard that executes a preprogrammed payload.
These types of devices, recognized as Human Interface Devices (HIDs) by computers, are generally trusted by all systems without raising security flags.
The payload can perform a range of tasks, from configuring network settings to installing a reverse shell, replicating the actions of an administrator in a terminal, but in just seconds.
This makes the device a powerful tool for automating system administration tasks and an essential asset in penetration testing.
BadUSB (rubber ducky)

## Slide 11
This keystroke injection device operates using an STM32F072C8T6 microcontroller along with a flash memory chip that emulates a mass storage device.
When the device is connected to a computer, the microcontroller boots and searches the FAT32-formatted storage (open-source) for a specific file containing the preprogrammed payload.
Once the file is located, the microcontroller decodes the instructions into simulated keyboard presses and mouse movements.
This allows the device to automate complex tasks by mimicking human input, making it a highly efficient tool for executing scripted commands quickly, reliably and covertly.

## Slide 13
We used AI to:

## Slide 14
Stealthy Logic: Keyboard Injection to Verilog State Machine Trojan for Conditional DoS
1st design

## Slide 15
DoS Attack Conditions:
  State Machine Insertion: The modified Verilog code includes a state machine that monitors for specific conditions (e.g., receiving a certain bit pattern over UART).
  DoS Trigger: Once the condition is met, the state machine causes the hardware to enter a malfunctioning or infinite loop state, effectively creating a denial-of-service condition.
Execution Flow and DoS Trigger
Key Result: Hardware becomes unresponsive or malfunctions under specific inputs.

## Slide 16
AXI stream UART peripheral
Normal Operation

## Slide 17
AXI stream UART peripheral
Infected Hardware

## Slide 18
Goal: Insert a software trojan via a BadUSB device (keyboard injection) to modify a hardware design and execute a Denial-of-Service (DoS) attack.
Target: A Verilog-based open-source hardware design (e.g., OpenCores or OpenTitan).
Key Attack Stages:
BadUSB Delivery: The trojan is delivered through a BadUSB device, which injects a payload into the victim's system.
Trojan Deployment: The trojan searches for Verilog files related to the target hardware (UART perpheral).
DoS Mechanism: The trojan modifies the Verilog design, inserting a state machine that triggers a DoS attack when a specific condition is met (when a particular bit sequence in a UART transmission is detected).

## Slide 19
Impact:
This type of attack can be subtle, hard to detect, and capable of crippling hardware functionality under specific, targeted conditions.
Severity of the Vulnerability:
Insertion Phase: Design stage
Abstraction Level: Register-transfer level (RTL)
Activation Mechanism: Conditionally triggered
Functional Effects: Causes a denial-of-service (DoS) attack
Physical Characteristics: Functional disruption
Impact and vuln. severity

## Slide 20
Cryptoleak: Subtle Timing Exploits for AES Key Extraction with Trojan Listeners
2nd design

## Slide 21
Goal: Covertly exfiltrate AES encryption keys by modulating the clock signal in a hardware design.
Target: AES IP core integrated into a PC, where the AES key is leaked through clock signal variations.
Attack Stages:
Trojan Introduction via BadUSB: The trojan modifies the AES Verilog core, causing subtle modulation of the clock signal during key scheduling or encryption.
Clock Modulation: The trojan encodes the AES key into small changes in the clock frequency, phase, or duty cycle during encryption operations.
Main Techniques:
  Clock Signal Modulation: Introducing slight variations (frequency or phase shifts) in the clock signal to encode key bits.
  BadUSB for Trojan Injection: Using BadUSB to inject a trojan that modifies the Verilog IP core.
Introduction

## Slide 22
AES Core IP Block
Normal Operation

## Slide 23
Infected Hardware
AES Core IP Block

## Slide 24
Trojan Design: The software trojan on the PC monitors the timing variations in the AES clock signal using the Time Stamp Counter (TSC) or other low-level timing facilities (e.g., PMU).
Timing Data Collection: The Trojan collects timing data during encryption and identifies small shifts that correspond to bits of the AES key.
Monitoring Process
Key Extraction:
Data Processing: Timing deltas (differences between normal clock cycles and modulated cycles) are processed to extract key bits.
Key Decoding: The software reconstructs the AES key based on the timing patterns.

## Slide 25
Flowchart of Trojan Operations:
  Trojan monitors timing variations during encryption.
  Timing shifts are detected and recorded.
  Extracted key bits are assembled to reconstruct the full AES key.
Demonstration
Impact:
This attack leverages hardware side-channels (timing variations) to steal sensitive information with minimal impact on system functionality, making it difficult to detect.
Severity of the Vulnerability:
Insertion Phase: Design stage
Abstraction Level: Register-transfer level (RTL)
Activation Mechanism: Subtle clock signal modulation
Functional Effects: Covert AES key exfiltration
Physical Characteristics: Timing-based side-channel leakage